## Slide 1: GiveWay: Adaptive Traffic Equity System (ATES) utilizing PCE-Weighted Dynamic Phasing
Presenters/Authors: Hari Haran T, Siddharth S, Vishnu Balaji C
Institution: NPR College of Engineering and Technology
Project Overview: A real-time, hardware-software integrated prototype for dynamic traffic signal control based on Passenger Car Equivalent (PCE) metrics.
Aim of the Presentation: To present the architectural design, hardware integration, and operational logic of the GiveWay prototype system.

## Slide 2: Introduction to the Problem Context
Urban Traffic Congestion: Rapid urbanization has led to increased vehicular density, rendering fixed-time traffic signal controllers inefficient for fluctuating traffic patterns.
Limitations of Static Timers: Pre-programmed traffic lights allocate equal green time regardless of the actual lane density, leading to empty lanes receiving green signals while congested lanes wait.
The Need for Adaptability: Modern intersections require systems that can read current traffic states and dynamically allocate right-of-way to optimize throughput.
Focus on Equity: Traffic management must account for the type of vehicles (e.g., a bus vs. a motorcycle) rather than just the raw count, to ensure true throughput equity.

## Slide 3: Proposed Solution: The GiveWay System
Core Concept: GiveWay is an Adaptive Traffic Equity System (ATES) designed to replace static timers with dynamic, real-time phase allocation.
PCE-Centric Approach: Utilizes Passenger Car Equivalent (PCE) weighting to calculate the actual spatial and temporal footprint of vehicles at an intersection, rather than simple vehicle counting.
Hybrid Architecture: Combines edge-level hardware control with cloud-ready backend logic to form a responsive, scalable traffic management node.
Prototype Scope: The current iteration focuses on proving the viability of the logic and hardware integration in a controlled, single-junction prototype environment (e.g., Dindigul junction model).

## Slide 4: Key System Objectives
Dynamic Phase Allocation: To construct a system capable of adjusting green light durations continuously based on live lane density inputs.
Hardware-Software Synchronization: To establish robust, low-latency communication between the traffic control hardware (Arduino/ESP32) and the decision-making backend (Node.js).
Emergency Vehicle Prioritization: To integrate hardware interrupts (RFID) that immediately grant right-of-way to critical emergency services.
Operator Override Capabilities: To provide authorized personnel with the ability to impose manual system states (VIP, Festival, All-Stop) via a centralized dashboard.

## Slide 5: System Architecture Overview
Master-Slave Topology: The system is built on a Master-Slave architecture where a central controller dictates phase changes to individual lane nodes.
Edge Hardware Layer: Comprises microcontrollers (Arduino Mega) handling direct electrical actuation of signal LEDs and reading local sensor data.
Decision Engine Layer: A Node.js backend operates as the brain, processing incoming lane data, executing the PCE algorithms, and broadcasting state commands.
Application Interface Layer: A React-based web dashboard and a Flutter/Dart mobile application provide real-time visualization and administrative control over the hardware states.

## Slide 6: Hardware Implementation Details
Primary Controller: Arduino Mega acts as the central hardware hub, chosen for its extensive GPIO pin availability necessary for multi-lane LED control.
Visual Indicators: Standard Red, Yellow, and Green LED arrays wired in parallel with custom countdown timer displays for each lane.
Vision Sensors: ESP32-CAM modules positioned at each lane approach to capture visual data of the current traffic state.
Emergency Detection: RFID readers integrated at the approach nodes to detect tagged emergency vehicles and trigger hardware-level interrupts.

## Slide 7: Software & Communication Stack
Backend Infrastructure: Built on Node.js and Express, providing a lightweight, non-blocking environment ideal for handling concurrent hardware requests.
Communication Protocols: Utilizes RESTful APIs for state configuration and WebSocket/Serial communication for real-time, low-latency telemetry streaming to the hardware.
Frontend Technologies: React.js is used for the web-based tactical dashboard, ensuring modular component design and rapid UI rendering.
Mobile Interface: Dart/Flutter framework utilized for the mobile application, ensuring cross-platform compatibility for on-the-go system monitoring.

## Slide 8: Core Logic: The PCE-Weighted Algorithm
What is PCE? Passenger Car Equivalent (PCE) assigns a standardized spatial value to different vehicle classes (e.g., Two-wheeler = 0.5, Car = 1.0, Bus = 3.0).
Density Calculation: The system aggregates the PCE values of all vehicles detected in a lane to determine the total "Weight" or "Density" of that lane.
Equity over Count: By using PCE, GiveWay ensures that a lane with two buses receives appropriate priority compared to a lane with three motorcycles, reflecting true spatial demand.
Algorithm Execution: The backend continuously recalculates the PCE density for all active lanes to determine the optimal next phase in the cycle.

## Slide 9: Dynamic Phase Allocation Mechanism
Continuous Polling: The master controller continuously polls the status of all four lanes at the junction.
Proportional Time Distribution: Base green time is dynamically extended or reduced proportionally to the calculated PCE density of the active lane.
Phase Skipping: If a lane registers a PCE density of zero (empty lane), the algorithm skips its phase entirely, preventing wasted green time.
Maximum Cap Limits: Hardcoded maximum green time caps are enforced to prevent starvation of lower-density lanes, ensuring eventual right-of-way for all approaches.

## Slide 10: Special Operational System Modes
VIP Corridor Mode: An administrative override that locks a specific route in a continuous green state to facilitate the uninterrupted movement of high-priority convoys.
Festival/Congestion Mode: A specialized algorithm state triggered during known high-volume events, adjusting base timings and caps to handle sustained, heavy throughput.
All-Stop / Emergency Halt: A global override that immediately forces all lanes to red, freezing the junction in the event of an accident or critical hazard.
Mode Switching: These modes bypass the standard dynamic algorithm and directly actuate the hardware via the backend override API.

## Slide 11: Emergency & Priority Routing
Hardware Interrupts: RFID tags placed on emergency vehicles (ambulances, fire engines) trigger an immediate hardware interrupt when read by the lane sensors.
Preemption Sequence: Upon detection, the system initiates a safe transition sequence (Yellow to Red) for currently active lanes.
Targeted Green Phase: The specific lane containing the emergency vehicle is granted an immediate, locked green phase until the vehicle clears the intersection.
State Restoration: Once the RFID tag is no longer detected in the clearance zone, the system seamlessly resumes the standard PCE-weighted dynamic cycle.

## Slide 12: Real-time Monitoring and Interfaces
Tactical Web Dashboard: A React-based interface providing administrators with a live, visual replica of the physical intersection's state.
Live Telemetry: Displays current lane statuses, active countdown timers, and the operational mode currently engaged by the backend.
Incident Tracking: Features a "Ghost-Lane" monitor and incident logging system to track anomalies or manual overrides.
Mobile Accessibility: The Flutter app mirrors the critical monitoring functions of the web dashboard, providing field operators with live status updates.

## Slide 13: System Advantages and Robustness
Edge-Level Reliability: By utilizing Arduino for direct actuation, the physical light switching remains stable even if backend cloud connectivity experiences momentary latency.
Scalable Architecture: The Node.js and REST/Socket stack allows the single-junction logic to be scaled to a multi-junction network without changing the core edge hardware.
Modular Design: The separation of hardware actuation (Arduino), decision logic (Node), and presentation (React) ensures easy maintenance and future feature additions.
Real-world Applicability: The system is designed using readily available, cost-effective components, making it a highly viable prototype for developing nations' traffic infrastructure.

## Slide 14: Challenges and Implementation Constraints
Hardware Limitations: Prototype hardware (Arduino/ESP32) possesses inherent processing and memory constraints compared to industrial-grade PLC controllers.
Environmental Factors: Optical sensors (ESP32-CAMs) are susceptible to environmental noise (glare, heavy rain, low light), requiring robust physical enclosures in a real-world scenario.
Algorithm Boundary Cases: Fine-tuning the minimum and maximum green time caps requires extensive field observation to prevent edge-case starvation scenarios.
Future Scope (AI Integration): While the current system relies on direct PCE calculation logic, future iterations could integrate trained machine learning models for predictive traffic routing.

## Slide 15: Conclusion
Project Summary: The GiveWay ATES successfully demonstrates a working prototype of a dynamically adaptive traffic control system.
Achieved Goals: We have successfully integrated edge hardware, a centralized decision engine, and real-time monitoring interfaces into a cohesive ecosystem.
Proof of Concept: The prototype validates the concept that PCE-weighted algorithms can be effectively translated into physical hardware actuation.
Final Statement: GiveWay provides a robust, scalable architectural foundation for modernizing urban traffic infrastructure to be more equitable, responsive, and efficient.